EPICS Database Practice
Andrew Johnson
APS Engineering Support Division
January 2007
USPAS EPICS Course

---
EPICS record types
Where do record types come from?
  - EPICS Base (<base>/src/rec)
    - General purpose record types
    - No record-type specific operator displays or databases
    - Documentation in EPICS Record Reference Manual
  - EPICS collaboration
    - General purpose, and application-specific, record types
    - Some are supported for use by collaborators (some are NOT)
    - Some come with record-type specific displays, databases
  - Custom record types can be written by an EPICS developer, and added to an EPICS application.
    - Not in the scope of this lecture

---
The Record Reference Manual
Where is it?
  - EPICS Home > Base > R3.13 > Reference Documents (html)
What is in it?
  - Database Concepts (good review)
  - Fields common to all records (covered earlier)
  - Fields common to many records (covered earlier)
  - Record Types – provides a description of the record processing routines for most of the record types in base.
When would I use it?
  - Skim through before writing any databases
  - Read through before writing any records
  - Otherwise, use as reference

---
Manual Outline
Preface, Chapter 1: Essential background information
  - Note special meaning of the words scan, process, address, link, and monitor
Chapter 2-39: Record reference
  - Somewhat out of date
  - Descriptions of record fields, processing, and useful info for writing device support
  - Contains lots of tables like the following:
No
No
Yes
Yes
Null
Yes
STRING [29]
Description
DESC
No
No
No
Yes
Null
Yes
STRING [29]
Record Name
NAME
No
No
Yes
Yes
0
Yes
SHORT
Display Precision
PREC
No
No
Yes
Yes
0
Yes
FLOAT
Low Operating Range
LOPR
No
No
Yes
Yes
0
Yes
FLOAT
High Operating Range
HOPR
No
No
Yes
Yes
null
Yes
STRING [16]
Engineering Units
EGU
PP
Rec Proc Monitor
Modify
Access
Initial
DCT
Type
Summary
Field

---
Collaboration supported records
Where are they found?
  - Soft-support list: http://www.aps.anl.gov/epics/modules/soft.php
  - The tech-talk email list
  - The soft-support list contains entries like this (among entries for other kinds of soft support):
SLAC:time stamp
Stephanie Allison
...exports its timestamp as a string
timestamp
record
APS:synApps/optics
Tim Mooney
Control an optical table
table
record
...
...
...
...
...
OSL:epics
Andy Foster
Multi-I/O subroutine, handles arrays
genSub
record
CARS:epid Record
Mark Rivers
Enhanced PID record
epid
record
Link
Contact
Description
Name
Class

---
Input Records
ai - Analog input [BASE]
  - Read analog value, convert to engineering units, four alarm levels, simulation mode
aai – Array analog input [BASE]
  - Read array of analog values, simulation mode
bi - Binary input [BASE]
  - Single bit, two states, assign strings to each state, alarm on either state or change of state, simulation mode
mbbi - Multi-bit binary input [BASE]
  - Multiple bit, sixteen states, assign input value for each state, assign strings to each state, assign alarm level to each state, simulation mode
mbbiDirect – mbbi variant [BASE]
  - Read an unsigned short and map each bit to a field (16 BI records in one)

---
Input Records (cont..)
stringin - String input [BASE]
  - 40 character (max) ascii string, simulation mode
longin - Long integer input [BASE]
  - Long integer, four alarm levels, simulation mode
waveform – array input [BASE]
  - Configurable data type and array length (16,000 bytes max for CA in EPICS 3.13)
mbbi32Direct [ORNL] longMbbiDirect [KEK] – 32-bit mbbiDirect
  - Read an unsigned long and map each bit to a field (32 BI records in one)
mca – multichannel analyzer [synApps]
  - Supports multichannel analyzers, multichannel scalers, and other array-input hardware

---
Input Records (cont..)
pulseCounter [ANL RecRefMan]
  - Written to support a Mizar 8310 timing module
scaler [synApps]
  - Controls a bank of counters
swf [BESSY] , wftime [SLAC] – waveform variants
  - Includes scaling and time (wftime) information
timestamp [SLAC]
  - Exports its timestamp as a string

---
Algorithms/Control Records - Calc
calc - run-time expression evaluation [BASE]
  - 12 input links, user specified “calc expression” (algebraic, trig, relational, Boolean, Logical, “?”), four alarm levels
  - Sample expressions:
    - 0 read: “<calc_record>.VAL = 0”
    - A note ‘A’ refers to <calc_record>.A
    - A+B
    - sin(a)
    - (A+B)<(C+D)?E:F+L+10
calcout – calc variant [BASE]
  - Conditional output link, separate output CALC expression (.OCAL), output delay, and output event
  - Output-link options : "Every Time”, "On Change", "When Zero", "When Non-zero", "Transition To Zero", "Transition To Non-zero“

---
Algorithms/Control Records - Calc
sCalcout – calcout variant [synApps]
  - Has both numeric fields (A,B,..L) and string fields (AA,BB,..LL)
  - Supports both numeric and string expressions. E.g.,
    - A+DBL(“value is 3.456”) -> 4.456
    - printf(“SET:VOLT:%.2lf”, A+4) -> “SET:VOLT:5.00”
  - Additional output-link option: “Never”
transform – calc/seq variant [synApps]
  - Like 16 calcout records (but outlinks are not conditional)
  - Expressions read all variables, but write to just one.
  - Uses sCalcout record’s calculation engine
  - Example expressions:
    - A: 2 read: “<transform>.A = 2”
    - B: A+1+C uses new value of ‘A’, old value of ‘C’

---
Algorithms/Control Records - Array
compress [BASE]
  - Input link can be scalar or array.
  - Algorithms include N to 1 compression (highest, lowest, or average), circular buffer of scalar input.
histogram [BASE]
  - Accumulates histogram of the values of a scalar PV
subArray [BASE]
  - Extracts a sub-array from a waveform.
aConcat [KEK], joinArray [SLS]
  - Concatenate waveforms
genSub – sub variant [OSL]
  - Multiple inputs and outputs
  - Handles arrays and structures

---
Algorithms/Control Records – List
dfanout – Data fanout [BASE]
  - Writes a single value to eight output links
fanout [BASE]
  - Forward links to six other records.
  - Selection mask
sel - Select [BASE]
  - 12 input links, four select options [specified, highest, lowest, median], four alarm levels
seq - Sequence [BASE]
  - Ten “Input link/Value/Output link” sets: [inlink, delay, value, outlink]
  - Selection mask

---
Algorithms/Control Records – List
lseq – seq variant [JACH]
  - 16 sets, instead of 10
sseq – seq variant [synApps]
  - seq record for string or numeric data
  - optional wait for completion after each set executes
wfselector – waveform/sel variant [KEK]
genSub [OSL]
sCalcout [synApps]
transform [synApps]

---
Algorithms/Control Records - Loop
scan [ANL]
  - Four “positioners”, two “detector triggers”, fifteen “detectors”.
  - Systematically sets conditions, triggers detectors, and acquires data into arrays.
  - Database detects completion and drives scan to next step.
sscan – scan variant [synApps]
  - Uses ca_put_callback() to detect completion.
  - Four triggers, 70 detector signals (arrays, scalars, or mixed)
  - Array-prepare trigger at end of scan
  - 2000 data points in EPICS 3.13; “unlimited” number in EPICS 3.14
  - Supports scan pause; before/after-scan action; move-to-peak.
  - Handshake permits data-storage client to write old data while new data is being acquired.

---
Algorithms/Control Records - Subroutine
sub – Subroutine [BASE]
  - 12 input links, user provided subroutine, four alarm levels
genSub – sub variant [OSL]
  - Multiple inputs and outputs
  - Handles arrays and structures

---
Algorithms/Control Records - Other
event [BASE]
  - Posts a “soft” event which may trigger other records to process.
  - Simulation mode
PID [ANL], CPID [JLAB], EPID [synApps]
  - Proportional/Integral/Derivative Control
pal [3.13 BASE]
  - Emulates Programmable Array Logic
cvt – ai/ao variant [BESSY]
  - 1 or 2 inputs, 1 output, conversion types: linear, subroutine, 1D or 2D table
Permissive – handshake [BASE]
  - Implements a client-server handshake
state – string state value [BASE]
  - Implements a string, for client-server communication

---
Output Records
ao - Analog output [BASE]
  - Write analog value, convert from engineering units, four alarm levels, closed_loop mode, drive limits, output rate-of-change limit, INVALID alarm action, simulation mode
aao – Array analog output [BASE]
  - ao for arrays
bo - Binary output [BASE]
  - Single bit, two states, assign strings to each state, alarm on either state or change of state, closed_loop mode, momentary ‘HIGH’, INVALID alarm action, simulation mode
longout [BASE]
  - Write long integer value, four alarm levels, closed_loop mode, INVALID alarm action, simulation mode

---
Output Records (cont..)
mbbo - Multi-bit binary output [BASE]
  - Multiple bit, sixteen states, assign output value for each state, assign strings to each state, assign alarm level to each state, closed_loop mode, INVALID alarm action, simulation mode
mbboDirect - mbbo variant [BASE]
  - 16 settable bit fields that get written as a short integer to the hardware, closed_loop mode, INVALID alarm action, sim. mode
mbbo32Direct - mbbo variant [ORNL]
longMbboDirect - mbbo variant [KEK]
  - 16 settable bit fields that get written as a long integer, closed_loop mode, INVALID alarm action, simulation mode
motor [synApps]
  - Controls stepper and servo motors
  - Has its own lecture (Motors)

---
Output Records (cont..)
steppermotor [3.13 BASE]
  - Position control, retry, speed, ramps, etc
pulseDelay [3.13 BASE]
  - Written to support a Mizar 8310 timing module
pulseTrain [3.13 BASE]
  - Written to support a Mizar 8310 timing module
stringout [BASE]
  - Write a character string (40 max), closed_loop mode, INVALID alarm action, simulation mode

---
Examples of Custom Records
rf - RF Amplitude Measurements [ANL]
  - Sample time, measurement in watts and db, waveform acquired through sweeping sample time
bpm - Beam Position Monitor [ANL]
  - Four voltage inputs, numerous calibration constants, X-Y-I outputs, waveforms for each input
Many others that are site-specific

---
Which record is right for …
Soft parameters entered by an operator
  - AO has DRVH, DRVL, OROC, closed loop
  - MBBO provides enumerated options which can be converted to constants (use DTYP = Raw Soft Channel)
  - Normally one does not use input records for this purpose
Multiple output actions
  - Sequence record can have a different data source for each output link vs. the dfanout record which “fans out” a single source to multiple links
Different output actions based on an operator selection
  - CALCOUT records that conditionally process sequence records
  - MBBO (Soft Raw Channel) forward linked to a single sequence record in “masked” mode. Mask is provided in MBBO for each state.

---
Defining the Database
How does an IOC know what record types and device support options are available ?
  - Record types, device support options, choice menus, and other configuration options are defined in Database Definition files (.dbd)
  - During the IOC boot process, one or more .dbd files are loaded
  - The .dbd files define the software configuration for that IOC
How does an IOC know about record instances (the user’s database) ?
  - Record instances are describe in Database files (.db)
  - During the IOC booting process, one or more .db files are loaded
  - The .db files define the record instances for that IOC

---
Database Definition File
menu(menuPriority) {
  choice(menuPriorityLOW,"LOW")
  choice(menuPriorityMEDIUM,"MEDIUM")
  choice(menuPriorityHIGH,"HIGH")
}
menu(menuScan) {
  choice(menuScanPassive,"Passive")
  choice(menuScanEvent,"Event")
  choice(menuScanI_O_Intr,"I/O Intr")
  choice(menuScan10_second,"10 second")
  choice(menuScan5_second,"5 second")
  choice(menuScan2_second,"2 second")
  choice(menuScan1_second,"1 second")
  choice(menuScan_5_second,".5 second")
  choice(menuScan_2_second,".2 second")
  choice(menuScan_1_second,".1 second")
}
device(ai,CONSTANT,devAiSoftRaw,
        "Raw Soft Channel")
device(ai,BITBUS_IO,devAiIObug,
        "Bitbus Device")
device(ao,CONSTANT,devAoSoftRaw,
        "Raw Soft Channel")
device(ao,VME_IO,devAoAt5Vxi,
        "VXI-AT5-AO")
device(bi,VME_IO,devBiAvme9440,
        "AVME9440 I")
device(bi,AB_IO,devBiAb,
        "AB-Binary Input")
driver(drvVxi)
driver(drvMxi)
driver(drvGpib)
driver(drvBitBus)
Extracts from a typical .dbd file

---
Database Definition File continued...
menu(aoOIF) {
 choice(aoOIF_Full,"Full")
 choice(aoOIF_Incremental,
        "Incremental")
}
recordtype(ao) {
  include "dbCommon.dbd"
  field(VAL,DBF_DOUBLE) {
    prompt("Desired Output")
    promptgroup(GUI_OUTPUT)
    asl(ASL0)
    pp(TRUE)
  }
  field(OUT,DBF_OUTLINK) {
   prompt("Output Specification")
   promptgroup(GUI_OUTPUT)
   interest(1)
 }
  field(OIF,DBF_MENU) {
   prompt("Out Full/Incremental")
   promptgroup(GUI_OUTPUT)
   interest(1)
   menu(aoOIF)
  }
 field(OVAL,DBF_DOUBLE) {
    prompt("Output Value")
  }
 field(PREC,DBF_SHORT) {
   prompt("Display Precision")
   promptgroup(GUI_DISPLAY)
   interest(1)
 }
 ...
}
Parts of the ao record type definition from a typical .dbd file

---
Database File
record(bo,"$(user):gunOnC") {
    field(DESC,"Controls e-gun")
}
record(bo,"$(user):gunOnC") {
    field(DESC,"Controls e-gun")
    field(DTYP,"Soft Channel")
    field(ZNAM,"Beam Off")
    field(ONAM,"Beam On")
}
record(ao,"$(user):cathodeCurrentC") {
    field(DESC,"set cathode current")
    field(DTYP,"Raw Soft Channel")
    field(SCAN,"1 second")
    field(OROC,".5")
    field(PREC,"2")
    field(EGU,"Amps")
    field(DRVH,"20")
    field(DRVL,"0")
    field(HOPR,"20")
    field(LOPR,"0")
}
record(calc,"$(user):rampM") {
    field(CALC,"A>6.27?0:A+.1")
    field(SCAN,"1 second")
    field(INPA,"$(user):rampM.VAL")
}
record(calc,"$(user):cathodeTempM") {
    field(DESC,"Measured Temp")
    field(SCAN,"1 second")
    field(CALC,"C+(A*7)+(SIN(B)*3.5)")
    field(INPA,"$(user):cathodeCurrentC.OVAL")
    field(INPB,"$(user):rampM.VAL")
    field(INPC,"70")
    field(EGU,"degF")
    field(PREC,"1")
    field(HOPR,"200")
    field(LOPR,"")
    field(HIHI,"180")
    field(LOLO,"130")
    field(HIGH,"160")
    field(LOW,"140")
    field(HHSV,"MAJOR")
    field(HSV,"MINOR")
    field(LLSV,"MAJOR")
    field(LSV,"MINOR")
}

---
Loading Database Files into the IOC
A typical startup script (st.cmd) might contain
  - dbLoadDatabase("../../dbd/linacApp.dbd")
  - dbLoadRecords("../../db/xxLinacSim.db","user=studnt1")
  - iocInit /* starts database processing */
One or more database definition files (.dbd) must be loaded first.
  - Any record type used in the database files must have been defined in the definition file
Values for macros used within the database file (e.g. $(user) ) can be specified when loading. This allows a database to be loaded more than once with different record names and I/O addresses each time

---
Creating Database Files
Since the database file is a simple ascii file, it can be generated by numerous applications … as long as the syntax is correct
  - Text editor
  - Script (Perl, Python, shell, awk, sed, …)
  - Relational Database
  - EPICS-aware Database Configuration Tools:
    - VDCT (recommended for new designs)
    - CAPFAST (a schematic entry application)
    - JDCT (not graphical)
    - GDCT (no longer supported)
An EPICS-aware tool will read the .dbd file (library provided) and provide menu selections of enumerated fields. It may also detect database errors prior to the boot process
A graphical tool is helpful for complex databases

---
Database Examples
Calculating “Rate-of-Change” of an Input
INPA fetches data that is 1 second old because it does not request processing of the AI record. INPB fetches current data because it requests the AI record to process. The subtraction of these two values reflects the ‘rate of change’ (difference/sec) of the pressure reading.

---
Database Examples
When in simulation mode, the AO record does not call device support and the AI record fetches its input from the AO record.

---
Database Examples
Maximize Severity
If chassis is powered off, Temp Trip and Flow Trip indicate Normal. Force these PVs into an alarm state by specifying .SDIS with .MS (maximize severity) to the Chassis On record. Set .DISV (disable value) to 2 so processing will never be disabled.

---
Database Examples
Slow Periodic Scan with Fast Change Response
The AI record gets processed every 5 seconds AND whenever the AO record is changed. This provides immediate response to an operator's changes even though the normal scan rate is very slow. Changes to the power supply settings are inhibited by the BO record, which represents a Local/Remote switch.

---
Database Examples
Different Actions Based on Operator Selection
record(mbbo,"$(user):PS:Control") {
        field(DTYP,"Raw Soft Channel")
        field(FLNK,"$(user):PS:ControlSQ.VAL PP NMS")
        field(ZRVL,”0x3") BIT MAP: 0000000000000011 -> do LNK1, LNK2
        field(ZRST,"Off") menu item operator sees
        field(ONVL,”0x5") BIT MAP: 0000000000000101 -> do LNK1, LNK3
        field(ONST,"On)") menu item operator sees
        field(TWVL,"0xc") BIT MAP: 0000000000001100 -> do LNK3, LNK4
        field(TWST,"Set @ Default") menu item operator sees
}
record(seq,"$(user):PS:ControlSQ") {
        field(SELM,"Mask")
        field(SELL,"$(user):PS:Control.RVAL NPP NMS")
        field(DLY1,"0")
        field(DOL1,"0")
        field(LNK1,"$(user):PS:setCurrent.VAL PP NMS")
        field(DLY2,"2")
        field(DOL2,"0")
        field(LNK2,"$(user):PS:pwrControl.VAL PP NMS")
        field(DLY3,"0")
        field(DOL3,"1")
        field(LNK3,"$(user):PS:pwrControl.VAL PP NMS")
        field(DLY4,"1")
        field(DOL4,"3.75")
        field(LNK4,"$(user):PS:setCurrent.VAL PP NMS)
}
Off
On
Set @ Default
Different links in the sequence record are executed for each selection of the mbbo. This allows much functionality to be specified in only two records.

---
Database Examples
Automatic Shutdown on Logout
If no CA monitor exists on the SUB record (i.e. the operator logs out), MLIS will be NULL. The subroutine will then set the .VAL field to 0, causing the sequence record to process.

---
Database Examples
Quick Prototyping with Standard Records
Custom Record Definition
Left BPM Button
.INPL
.XPOS
BPM Record
Right BPM Button
.YPOS
.INPR
- Average inputs
- Input history
- Standard deviation
...
.INT
Top BPM Button
.INPT
.VAL
Bottom BPM Button
.INPB