Getting Started with EPICS Lecture Series
Introduction to EPICS
John Maclean, Argonne National Laboratory

---
Overview
Overview
- Lay the foundation for understanding an EPICS control system
- Introduce IOCs
  - Channel Access (CA)
  - Database
  - Sequencer
  - Device Support
- Choosing the correct tools for the job
  - When to use a database
  - The sequencer, what is it good for?
  - Why write your own CA client program?
- How fast is EPICS?

---
Canonical Form of an EPICS Control System
Canonical Form of an EPICS Control System
Client Software
MEDM
OAG Apps
StripTool
ALH
TCL/TK
Many, many others
Perl Scripts
Channel Access
IOC Software
EPICS Database
Custom Programs
Sequence Programs
Commercial Instruments
Custom Chassis/Panels
Real-time
Control
Technical Equipment
CA Server Application
Process Variables
IOC
IOC
IOC
IOC
CAS
CAS

---
Introducing the IOC
Introducing the IOC
- Input Output Controller
- A computer running software called “IOC Core”
- The computer can be:
  - VME based, running vxWorks, RTEMS, Linux
  - PC running Windows, Linux, RTEMS
  - Mac running OSX
  - Embedded processor running RTEMS, Linux
- Usually has Input and/or Output devices attached
- An EPICS control system must consist of at least one Channel Access Server (usually an IOC)
- An IOC has one or more databases loaded. The database tells it what to do

---
Inside an IOC
Inside an IOC
The major software components of an IOC (IOC Core)
LAN
Channel Access
IOC
Sequencer
Database
Device Support
I/O Hardware

---
Channel Access
Channel Access
- Allows other programs (CA Clients) to see and change values of Process Variables in an IOC (CA Server)
- CA Clients may
  - Put (write)
  - Get (read)
  - Monitor
  data of Process Variables
- IOCs are both CA clients and CA servers. They can interact with data in other IOCs
- A CA Client can connect to many servers
- A CA Server may serve many clients
- A very efficient an reliable protocol
Workstation
Network
IOC
CA Server
CA Client

---
Inside an IOC
The major software components of an IOC (IOC Core)
LAN
Channel Access
IOC
Sequencer
Database
Device Support
I/O Hardware

---
EPICS Databases – What are they for?
EPICS Databases – What are they for?
- Interface to process instrumentation
- Distribute processing
- Provide external access to all process information
- Use common, proven, objects (records) to collect, process and distribute data
- Provide a common toolkit for creating applications

---
What are records?
What are records?
- A record is an object with
  - A unique name
  - Properties (fields) that contain information (data)
  - The ability to perform actions on that data
- A personnel record in a relational database has a name, and fields containing data
Unique record name
XYZ1234
Employee: James Bond
Badge # : 007
Address : Whitehall, London
Salary : £70070.07
Data
Fields

---
What are EPICS records?
What are EPICS records?
- A record is an object with…
  - A unique name e.g. S28:waterPressure
  - Controllable properties (fields) e.g. EGU
  - A behavior - defined by its record type
  - Optional associated hardware I/O (device support)
  - Links to other records
- Each field can be accessed individually by name
- A record name and field name combined give a the name of a process variable (PV)
- A Process Variable name is what Channel Access needs to access data

---
A Process Variable name
A Process Variable name
- A PV name is comprised of two parts
  - The record name, and
  - A the name of a field belonging to that record
- For example…
L1:water:temperature
.
EGU
A Process variable name
A record name
A dot to join them
A field name
Note that if no field name is given, Channel Access will default to using the .VAL field
i.e. to CA, “L1:water:temperature” = “L1:water:temperature.VAL”

---
What do records do?
What do records do?
- Records are active, they do things
  - Get data from other records or from hardware
  - Perform calculations
  - Check values are in range and raise alarms
  - Put data to other records or to hardware
  - Activate or disable other records
  - Wait for hardware signals (interrupts)
- What a record does depends upon its type and the values in its fields
- A wide range of records have already been created
- New record types can be added to a new application as needed
- A record does nothing until it is processed

---
Record types
Record types
- Classified into four general types
- Input: e.g.
  - Analog In (AI)
  - Binary In (BI)
  - String In (SI)
- Algorithm/control: e.g.
  - Calculation (CALC)
  - Subroutine (SUB)
- Output: e.g.
  - Analog Out (AO)
  - Binary Out (BO)
- Custom: e.g.
  - Beam Position Monitor
  - Multi Channel Analyzer

---
Some record types
Some record types
- Analog in
- Analog out
- Binary in
- Binary out
- Calculation
- Calculation out
- Compression
- Data fanout
- Event
- Fanout
- Histogram
- Motor
- Multi bit binary input
- Multi bit binary output
- PID control
- Pulse counter
- Pulse delay
- Scan
- Select
- Sequence
- String in
- String out
- Subarray
- Subroutine
- Waveform

---
Graphical view of a record
Graphical view of a record

---
IOC view of a record
IOC view of a record
record(ao,"DemandTemp") {
field(DESC,"Temperature")
field(ASG,"")
field(SCAN,"Passive")
field(PINI,"NO")
field(PHAS,"0")
field(EVNT,"0")
field(DTYP,"VMIC 4100")
field(DISV,"1")
field(SDIS,"")
field(DISS,"NO_ALARM")
field(PRIO,"LOW")
field(FLNK,"")
field(OUT,"#C0 S0")
field(OROC,"0.0e+00")
field(DOL,"")
field(OMSL,"supervisory")
field(OIF,"Full")
field(PREC,"1")
field(LINR,"NO CONVERSION")
field(EGUF,"100")
field(EGUL,"0")
field(EGU,"Celcius")
field(DRVH,"100")
field(DRVL,"0")
field(HOPR,"80")
field(LOPR,"10")
field(HIHI,"0.0e+00")
field(LOLO,"0.0e+00")
field(HIGH,"0.0e+00")
field(LOW,"0.0e+00")
field(HHSV,"NO_ALARM")
field(LLSV,"NO_ALARM")
field(HSV,"NO_ALARM")
field(LSV,"NO_ALARM")
field(HYST,"0.0e+00")
field(ADEL,"0.0e+00")
field(MDEL,"0.0e+00")
field(SIOL,"")
field(SIML,"")
field(SIMS,"NO_ALARM")
field(IVOA,"Continue normally")
field(IVOV,"0.0e+00")
}

---
EPICS Databases – What are they?
EPICS Databases – What are they?
- A collection of one or more EPICS records of various types
- Records can be interconnected and are used as building blocks to create applications
- A data file that’s loaded into IOC memory at boot time
- Channel access talks to the IOC memory copy of the database

---
Our First Database
Our First Database
Channel Access Client
ProcTemp
.VAL = 45.5
.EGU = deg C
.STAT = Normal
Tell me about ProcTemp
IOC
Channel Access Server
Analog to Digital Converter
Process
Temperature Sensor
Database
Analog In
ProcTemp
45.5 deg C
45.5°C
4.55V
116 counts
INP
VAL
EGU : deg C
EGUL: 0
EGUF: 100
Normal Operation
5 - 50°C
0 – 100°C
0 – 10V
8 bit ADC
0 – 10V
0 – 255 bits
HIGH: 51

---
Record Processing
Record Processing
- Record processing can be periodic or event driven
- Periodic: Standard scan rates are…
  - 10, 5, 2, 1, 0.5, 0.2 and 0.1 seconds
  - Custom scan rates can be configured up to speeds allowed by operating system and hardware
- Event driven: Events include
  - Hardware interrupts
  - Request from another record via links
  - EPICS Events
  - Channel Access Puts

---
Database Processing
Database Processing
IOC
ADC
Database
Analog In
L1:water:temp1
INP
VAL
Binary I/O
Problem:
In the LINAC we have a water chiller that must be turned ON whenever the average temperature of two temperature sensors rises above a set point. The set point is nominally 10 degrees centigrade.
Calculation
Binary out
EGU: deg C
L1:water:tempChk
L1:water:chillerCtl
INPA
DOL
OUT
INPB
VAL
ADC
C: 10
Chiller
Analog In
CALC: ( (A+B)/2 ) > C
L1:water:temp2
SCAN: 10 second
INP
VAL
EGU: deg C
T2
Sensor
Sensor
T1

---
Inside an IOC
The major software components of an IOC (IOC Core)
LAN
Channel Access
IOC
Sequencer
Database
Device Support
I/O Hardware

---
The Sequencer
The Sequencer
- Runs programs written in State Notation Language (SNL)
- SNL is a ‘C’ like language to facilitate programming of sequential operations
- Fast execution - compiled code
- Programming interface to extend EPICS in the real-time environment
- Common uses
  - Provide automated start-up sequences like vacuum or RF where subsystems need coordination
  - Provide fault recovery or transition to a safe state
  - Provide automatic calibration of equipment

---
SNL implements State Transition Diagrams
SNL implements State Transition Diagrams
State A
Event
Transition
A to B
Action
State B

---
STD Example
State Transition Example
Start
Low vacuum
pressure > 5.1 uTorr
Open the valve
High vacuum
pressure < 4.9 uTorr
Close the valve

---
Inside an IOC
The major software components of an IOC (IOC Core)
LAN
Channel Access
IOC
Sequencer
Database
Device Support
I/O Hardware

---
Device Support
Device Support
- Device and driver support interface hardware to the database
- Examples of devices….
- VME cards
- ‘Network Attached Devices’
  - Motor controllers
  - Oscilloscopes
  - PLCs
- ‘Message-Based Devices’
  - USB or RS-232 serial devices
  - GPIB devices

---
Device Support
- Usually has to be written for ‘new’ hardware
- Good news – someone, somewhere has usually written support for your device, or a very similar one before
- See the EPICS web site for available support
- Or ask the EPICS community

---
When to use databases
When to use databases
- Hardware connection
- Real time performance – no network latencies
- Whenever a database is good enough
Advantages	Disadvantages
Simplify hardware connection	If you have device support
Configuring not programming.	You need to understand database use
Database is easily understood by other EPICS developers
Speed - All processing (often) in same machine

---
When to use the sequencer
When to use the sequencer
- For sequencing complex events
- E.g. Parking and unparking a telescope mirror
Photograph courtesy of the Gemini Telescopes project

---
When to use clients
When to use clients
- To interact with the control system
- Many already exist – EDM/CSS, ALH, Strip Tool, archiver etc.
- For data analysis or visualization
- Supervisory control
- E.g. to manage an accelerator

---
How fast is EPICS?
How fast is EPICS?
- Can be fast or slow, it depends how you use it!
- Use the correct tool for the job; Database, sequencer, custom code (IOC) or custom code (client)
- Ultimately speed depends upon hardware
- Some benchmarks*:
Machine	OS	CPU	Speed	Rec/sec	%CPU
MVME167	vxWorks	68040	33MHz	6000	50
MVME 2306	vxWorks	PPC604	300MHz	10000	10
MVME5100	vxWorks	PPC750	450MHz	40000**	10**
PC	Linux	PII	233MHz	10000	27
PC	Linux	P4	2.4GHz	50000	9
*Benchmark figures courtesy of Steve Hunt (PSI)
**Extrapolated from performance figures provided by L.Hoff, BNL
Database design and periodic scanning effect apparent system speed

---
Apparent performance
Apparent performance
IOC
ADC
Database
12°C
Analog In
Process Now
Process Now
L1:water:temp1
INP
VAL
Binary I/O
Calculation
ON
OFF
Binary out
EGU: deg C
L1:water:tempChk
L1:water:chillerCtl
12
INPA
DOL
OUT
INPB
VAL
14
ADC
SCAN: 10 second
C: 15
C: 10
C: 10
Actuator
Analog In
Chiller
CALC: ( (A+B)/2 ) > C
14°C
1
0
L1:water:temp2
SCAN: 10 second
INP
VAL
Process Now
EGU: deg C
T2
Sensor
Sensor
T1

---
The EPICS web site
The EPICS web site
- The central site for EPICS information
- Documentation
- CA Clients
- Device support
- Tech-talk
- http://www.aps.anl.gov/epics

---
Acknowledgements
Acknowledgements
- Andrew Johnson (APS-Controls)
- Bob Dalesio (LANL)
- Deb Kerstiens (LANL)
- Rozelle Wright (LANL)