## Slide 1: Advanced Monitor/Subscription Mechanisms
Ralph Lange
EPICS Collaboration Meeting
October 11, 2009

## Slide 2: Motivation
Things get faster Not all clients want all updates
Wide use of timing/event systems Clients want to get updates only during “interesting” system states

## Slide 3: Current Limitations
Update rate is configured in the database
  One setup for all clients
Existing timing/event system driver and support
  May cause records to process on event
  May set time stamps from hardware
  No filtering of updates for unrelated records

## Slide 4: Design Considerations
Channel Access protocol compatibility Changes create a lot of trouble
Modularity Small systems need small footprint
API Compatibility Don’t break existing 3rd party code

## Slide 5: Server-Side Plug-Ins
Event Queue
ring buffer
Record
Event Subscription field 1 flags
Event Queue
ring buffer
Channel Access Client 1
Channel Access Client 2
MLIS field 1
field 2 field 3 …
Channel Access Server
Event Task 1
Event Task 2
Event Subscription field 2 flags
Event Subscription field 3 flags
Event Subscription field 1 flags
Event Queue
ring buffer
Ethernet
Record processing or field changes cause event updates
One set of event queues per client
Client
IOC
Plug-In Layer
Stackable modules
  Inserted between the event subscription and the event queue
Configuration and Instantiation
  Client uses JSON modifiers in PV name
  Plug-in parses its own configuration

## Slide 6: Possible Uses
Update rate limiting
  Current.VAL{”rate”:{”min”:0.1, ”max”:0.5}}
System state correlation
  Current.VAL{”state”:{”while”:”injecting”}}
  Timing/event system sets and resets state
  Plug-in passes only updates while in “injecting” state
Event value filtering
  Current.VAL{”avg”:3}
Array data buffering
…

## Slide 7: Project Status and Schedule
Currently in design phase
Work by Andrew Johnson and Ralph Lange
Part of EPICS Base 3.15
Expected to be working summer 2010
First plug-ins will include
  Update rate limiter
  Event-derived system state correlator