## Slide 1
Diamond Light Source
Mark Heron
Head of Controls Group
A Decade of EPICS on Diamond

## Slide 2: Content
Introduce Diamond
Key Diamond events over past decade
Significant developments in EPICS over the past decade
Technologies for today
Consider future
A Decade of EPICS on Diamond
EPICS Collaboration Meeting 1st – 3rd May 2013

## Slide 3: Diamond Light Source Ltd
Diamond Light Source Ltd. is a Joint Venture Company.
Its shareholders are:
The Wellcome Trust is an independent charity funding research to improve human and animal health. It is the UK's largest non-governmental source of funds for biomedical research.
The Science and Technology Facilities Council is an independent, non-departmental public body.
86 %
14 %

## Slide 4: Diamond Accelerators
Diamond Control System Installation and Commissioning and Management
Linac Pulsed, 5Hz
0 MeV to 100 MeV 3 nC 15 nA
Booster Pulsed 5 Hz 100 MeV to 3 GeV 1.5 nC 3 mA
Storage Ring Continuous 3 GeV 1.5 nC to 0.5 µC 0.8 mA to 300 mA

## Slide 5: Beamline Science Villages

## Slide 8: Key Diamond Events Over Past Decade
2003
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
Beam Booster
Beam SR
Central Computing
FOFB Oper.
Linac Comm
Ph 2, 15 BLs
funded
Ph 3, 10 BLs Funded
1st Users
7 BL’s
Top Up
Oper
EPICS Meeting @ Diamond
First Controls Staff on Site
EPICS Meeting @ Diamond & ISIS
Ph 2 BLs Complete
Foundations complete

## Slide 9: Beamline Schedule
Operational (
Optimisation
Construction
Design

## Slide 10: Diamond 2003

## Slide 11: Original Control System Architecture
Linux RH 9.0/EL3
EPICS 3.13.9
VME and MVME5500
IP modules for most IO
Very conservative
  Reused proven solutions
Developed and deployed 260 IOCs and ~300k PVs in 3 years
  It just worked !!

## Slide 12: Support From Industry
Key to managing peak workload
Turnkey systems with EPICS
  Linac, RF Amplifiers, RF cavities, Girder alignment, Monochromators, Beamline optics
Today you can buy black boxes with EPICS
  Libera BPM, Motor controllers, Cryocoolers ......
Technical support available commercially
  Commissioning and development effort
  EPICS consultants
  Examples include Hytec Electronics, Observatory Science, CosyLab, Tessella, Dsoft,
Measure of maturity of EPICS

## Slide 13: 3.14
Gave VxWork independence
  Removed the $10k entry barrier
  Opened up EPICS to smaller projects
Marty tried to convince me to take 3.14.1 for the Diamond machine
  I felt there wasn't time.
Michael Abbott used 3.14.6 for Libera BPMs
Nick Rees used 3.14.7 for Diamond beamlines
Migrated all controls to 3.14.8.2 from 2009 and then to 3.14.11

## Slide 14: Serial Device/Protocol Support
A Decade of EPICS on Diamond
EPICS Collaboration Meeting 1st – 3rd May 2013
In 2001
  “Diamond Control Systems needed to support 2116 serial devices”
  Sharp intake of breath
Made we us think about this evaluate options
Selected Streamdevice
  Removed need for hard coding protocols
  Separation of the definition of protocol from EPICS record
  Worked very well
# Frequency is a float
# use ai and ao records
getFrequency {
out "FREQ?"; in "%f";
}
setFrequency {
out "FREQ %f";
@init { getFrequency; }
}

## Slide 15: Asyn
2003 Spring EPICS meeting Marty was soliciting interest in an asynchronous IO subsystem for IOCs
Asyn R1-0alpha2 released 2004
Enabled the move away from bus based IO
Abstraction of the hardware interface
Simplified Device development
Motor Record 1
drvMotorAsyn
devMotorAsyn
devAsynFloat64
Asyn Port
pmacAsynMotor
pmacAsynIPPort (interpose - optional)
VME or Socket or Serial Port interface
PMAC Motor Controller
AI
Asyn Octet

## Slide 16: Area Detector
Moved EPICS into data acquisition
  2D detectors, CCDs, pixel array detectors
Image processing structure
  Server side
  Plugin based
  Gives performance
  Configurable on the fly
  Controlled through EPICS
Range Detectors/Cameras support
Data Streams other than CA
  Fast file systems
    Lustre and GPFS 900 MB/sec
  ffmpegServer

## Slide 17: Photon Beam Control and Data Acquisition
Detector IF or Area Detector
Experiment/Detector
BL Vac
CA Server
BL PSS
CA Server
Detector
CA
Server
BL Motor
Drives CA
Server
Photon Beamline
Acc
CA
server
Storage Ring,
IDs, FEs
EPICS Apps EDM/Alarm/Arch
GDA
Applications
GDA Scripting
CA Client
GDA Server
GDA Client
High Performance
File System

## Slide 18: Linux
Linux
  Commercial from Red Hat
    Include RT extensions
  In-house built
X86 PCs
  Development
  Operations
  Compute Clusters
1U PCs for IOCs
  RT extensions
VME PPC
  Replacing VxWorks
ARMs processors
  Libera BPMs
  PSU controllers
Windows IOCs (~20)
  Mostly associated with detectors

## Slide 19: Ethernet
Extended beyond traditional client server to become the IO bus
  Replacing VME/cPCI
Ethernet attached IO
  ADCs/DACs/Cameras/ Motors/Detectors/PLCs/ PSUs
Segregate instrument subnets from Control Network (CA)
  Performance
  Management
  Ethercat non-IP
Loss the mechanical aspect of VME/cPCI
A Decade of EPICS on Diamond
EPICS Collaboration Meeting 1st – 3rd May 2013

## Slide 20: New Control System Architecture
GDA
Rem. I/O Modules
Terminal Servers
PMAC GeoBrick
GigE Protocol
EPICS IOC Server x86/Linux
Ethernet
Analogue & Digital I/O
RS232 & RS45
Motors
Cameras
EPICS Client
A Decade of EPICS on Diamond
EPICS Collaboration Meeting 1st – 3rd May 2013

## Slide 21: EPICS V4
In 2003 we tried to plan “EPICS2010”
  Out of which came .......
EPICS V4
  EPICS V4 session at this meeting
Extends capability of EPICS
  Services
  Data acquisition
Part of the future
  Importance of V3 interoperability

## Slide 22: Diamond 2013

## Slide 23: People
Work of many people
  Diamond Controls Group
  Industry
  EPICS Collaboration

## Slide 24
Thank you.
Questions?
A Decade of EPICS on Diamond
EPICS Collaboration Meeting 1st – 3rd May 2013