## Slide 1: Modularity and Integration of Instrument Control Hardware at the ESS
Thomas Gahl
Group Leader Motion Control & Automation
www.europeanspallationsource.se
October 23, 2014

## Slide 2: Outline
Neutron Production & Instruments at ESS
Modular Instrument Control Concept
Timing System for Synchronisation and Time Stamping
Requirements Motion Control
Organisational Challenges
Internal and external (in-kind) Interfaces
Status Motion Control
Achnowledgements

## Slide 3: Neutron Instrumentation
Target produces fast neutrons (several GeV, like IFMIF facility)
2 Moderators, slowing down the neutrons into meV and eV range
Neutron Instruments = Neutron Beam Lines
4 Groups of Instruments (different lengths)
p
Notes: Generic suite of instruments,
Groups with different lengths (30 to 160m)

## Slide 4: Time Structure of the Neutron Beam
3 ms
68 ms
14 Hz rep rate
71.4 ms cycle time
2.86 ms pulse time
4% duty cycle
200 – 2000 m/s
30.5 ms
30.5 ms
71 ms
t
d

## Slide 5: Long Neutron Instrument
160m
n
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
Notes: Clear a tendency for higher integration rates within an instrument, across instruments and across the facility
And this hits the reality in ESS instrumentation:
160m over 3 Halls
20 Chopper, remote diagnostics, preemptive maintenance (high availability)
In-kind, external suppliers, decentralised production

## Slide 6: Modular Instrument Control Concept
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
EPICS
Timing
160m
PSS
CB
CB
CB
CB
CB+
CB
CB
CB
CB
CB+
n
Notes: Backbone are the two networks for EPICS and timing,
Physically one subnet for each instruments, but connectivity to the whole facility
Timing based on Micro Research Finland: one Master generator + timing receiver in each box
Network + Boxes supplied by the Controls Division, Integration shared between Controls and Instrument Teams

## Slide 7: Modular Instrument Control Concept
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
EPICS
Timing
160m
PSS
Shutter
Chopper
Chopper
Collimation
Vacuum
CB
CB
CB
CB
CB+
CB
CB
CB
CB
CB+
n
Detector Movement
Sample
Environment

## Slide 8: Modular Instrument Control Concept
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
EPICS
Timing
Detector
160m
Monitors
PSS
Shutter
Chopper
Chopper
Collimation
Vacuum
CB
CB
CB
CB
CB+
CB
CB
CB
CB
CB+
n
Detector Movement
Sample
Environment

## Slide 9: Modular Instrument Control Concept
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
EPICS
Timing
Detector
160m
Monitors
PSS
Shutter
Chopper
Chopper
Detector Movement
Sample
Environment
Collimation
Vacuum
CB
CB
CB
CB
CB+
CB
CB
CB
CB
CB+
Instrument Control, Data Acquisition, GUI
n
Notes: 3 Layers:
Bottom: local control SW for fast control loops and MPS
Middle: EPICS as transport layer
Top: Instrument Control, Data Aggregator and GUI
Only the top layer brings all functionality together and relates them in the right way:
Example: detector movement
The readout of the detector (as channel number) is relative to its outlines and the transformation into the physical space of the instruments is possible with the help of the position readout from the motion control system and best done by this top layer

## Slide 10: Modular Instrument Control Concept
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
EPICS
Timing
Detector
160m
Monitors
PSS
Shutter
Chopper
Chopper
Collimation
Vacuum
CB
CB
CB
CB
CB+
CB
CB
CB
CB
CB+
Instrument Control, Data Acquisition, GUI
n
Detector Movement
Sample
Environment
What can (or has to) be done locally will be done locally
Clear functionalities and interfaces for a single box, avoid direct interconnects
Linked together by an already existing facility wide network infrastructure
Notes: Summ-Up:
Everything that can be done (or has to be done) locally will be done locally (in one of the colored boxes), everything that has to be related to signals or data from other boxes has to be time stamped and sent to the Instrument Control/ Data Acquisition layer
That gives clear functionalities and clear interfaces for single boxes, easy to specify and to bring in as in-kind contributions or from suppliers
All modules are linked together by the Instrument Control/ Data Acquisition Software, it’s a crucial part of the instrument and will be tailored to the needs of each instrument
That’s gives the flexibility necessary to adapt the same hardware to each of the ESS instruments: the hardware is done once and prepared for all future (hi-level) functionalities

## Slide 11: Diagnostics
Beam Transport & Conditioning Area
Beam Extraction + Bunker Area
Sample Area
EPICS
Timing
Detector
160m
Monitors
PSS
Shutter
Chopper
Chopper
Collimation
Vacuum
CB
CB
CB
CB
CB+
CB
CB
CB
CB
CB+
Instrument Control, Data Acquisition, GUI
n
3
2
1
Detector Movement
Sample
Environment

## Slide 12: Requirements on Timing System
Coupling of all timing to one single source
Everywhere in the facility available, (time-) compensated cable lengths
Jitter 10 ns, precision of time stamp 100 ns
Master Pulse, 14 Hz
Custom Pulse,
n x 14 Hz
Master Pulse with delay Δt n
Master CLOCK 88 Mhz
Δt n
Custom CLOCK i.e. 10 khz
t

## Slide 13: Motion Control: Time Stamping
Transfer absolute timing information from Control Box to the local HW control unit:
Synchronise a timer on the control unit
Timestamp in the control unit direct readings of the sensor with minimal latencies
Transfer the sensor readings through the Control Box into EPICS
Synchronously vs. asynchronously
Motion Control Unit
Timing
Control Box
EPICS
Clock
Pulse (14 Hz)
Motor
Encoder
Timer
Stamping
Command Interface
Notes: Introduce to functionalities in the control unit:
Timer + timestamping
Synchron: With a fixed sample rate, might be synchronised with 14 Hz or not, i.e. repetitive analog signal like oscillation or movement with constant speed
Asynchron: With a fixed delta of a value: Each time when the value changes a certain amount a sample is taken (more often with rapid changes)

## Slide 14: Motion Control: Time Stamping
Motion Control Unit
Control Box
EPICS
Command Interface
Clock
Pulse (14 Hz)
Motor
Encoder
Timer
Stamping
Driver
I/O
RT Field Bus
(i.e. ETHERCAT)
Timing
Transfer absolute timing information from Control Box to the local HW control unit:
Synchronise a timer on the control unit
Timestamp in the control unit direct readings of the sensor with minimal latencies
Transfer the sensor readings through the Control Box into EPICS
Synchronously vs. asynchronously
Local distribution of control unit functionalities with real time field busses

## Slide 15: Motion Control: Top Requirements
Time stamping + 14 Hz synchronisation
Multi-axes synchronisation
Free configurable trajectories
Decentralisation through field bus with real-time capabilities
Modular and scalable (in terms of performance and price)
Diagnostics (preemptive maintenance)
EPICS integration
Components for high radiation environment
Stepper motors, DC, DC brushless, piezo
Encoder inc. quad., abs. SSI, resolver, (analog), (BiSS-C)

## Slide 16: Organisational Challenges: Time Line
2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027
Construction
Operation
3
4
2
3
2
3
3
2
Instrument Development
Prepare & standardise technologies before instruments are built

## Slide 17: Organisational Challenges: Internal Interfaces
Strong interaction between machine and beam line tech groups
Building overlapping interfaces

## Slide 18: Organisational Challenges: Internal Interfaces
Strong interaction between machine and beam line tech groups
Building overlapping interfaces
CB
Instrument Control, Data Acquisition, GUI
Motion
Control
Sample
Environment
CB
ICS
Technology Groups
DMSC

## Slide 19: Organisational Challenges: Internal Interfaces
Strong interaction between machine and beam line tech groups
Building overlapping interfaces
CB
Instrument Control, Data Acquisition, GUI
Motion
Control
Sample
Environment
CB
ICS
Technology Groups
DMSC
Torsten
Bögershausen
Anders
Petersson
Timo Korhonen
Mark Hagen

## Slide 20: Organisational Challenges: External
17 European partner countries
70 % of Neutron Instrumentation is in-kind
Ranges from whole instruments to single modules
Strong standardisation necessary (hardware list)
+ good definition of functionality and interfaces
Support of partners in testing their modules

## Slide 21: Motion Control: Status
Started with Delta Tau Geobrick for Test Stands and Demonstrators
Market survey / Requirements catalog
First steps in practical evaluation (Delta Tau Powerbrick, Beckhoff)
Integration of a Beckhoff ETHERCAT system into EPICS (TwinCat)
First application as chopper control demonstrator

## Slide 22: Motion Control: A path to an ESS Standard
Hardware Harmonisation Work Group @ESS
Collecting use cases from stake holders
Refine requirements catalog
Select candidates for practical evaluation
Coordinate evaluation/selection with stake holders and collaborators
Workshop in 2015 (2nd half) >> common decision on MCU standard
Issue Standard Document Motor/Encoder
Issue Standard Document Motion Control Unit
Framework agreement with supplier (incl. possible deliveries to in-kind partners)

## Slide 23: Thanks to
Motion Control & Automation Group
(Anders Sandström, Paul Barron, Torsten Bögershausen, Markus Larsson)
Sample Environments Group
(Anders Petersson)
Integrated Control Systems Division, Detector Group, Chopper Group, DMSC
Other colleagues on various institutes and facilities
(among others: Mark Könnecke-PSI, Steve Cox-ISIS, Brian Nutter-Diamond)

## Slide 24: Thanks to
… and you!
Notes: Thank you very much and I’m open for questions…

## Slide 25: ESS Instrument Control - Details for Motion Control-
Thomas Gahl
Group Leader Motion Control & Automation
www.europeanspallationsource.se
September 16, 2014

## Slide 26: Synchronising Motion Control (multiple axes)
14 Hz pulse (to synchronise movements with neutron pulse)
10 kHz as masterclock (to synchronise multi-axes systems)
≈1 Hz or slower pulse + reading of the appropriated absolute time over EPICS (to synchronise internal timer)
Master Pulse, 14 Hz
Master CLOCK 88 Mhz
Custom CLOCK i.e. 10 khz
t
Master Pulse, 1 Hz

## Slide 27: Chopper Control Demo
Development of a motion control for a ¼ scale chopper model and integration in an EPICS environment; interfaces and functionality according to ESS standards
Demonstration model at IKON7 and DENIM conference in Munich, Germany
Screenshots of User Interfaces

## Slide 30: ESS Instrument Control - Use cases-
Thomas Gahl
Group Leader Motion Control & Automation
www.europeanspallationsource.se
September 16, 2014

## Slide 31: Taking data on the fly
+151
+651
Motion Control (positions)
+151
+651
+151
+651
+651
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
Detectors, Monitors (neutron events)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085
Custom CLOCK i.e. 10 khz
Notes: Use cases: Most obvious from Automation point of view: Why not move and take data at the same time? Each machine in the industry is doing…
Move one or even more axes at the same time, synchronised
And take Neutron data and motor positions at the same time
Automatic scans are possible where the speed is determined by the the count rate and the statistics and the sampling rate of the position by the wanted precision in space (for a given speed)
Non-linear relation between axes possible, something like constant energy scans

## Slide 32: Stroboscopic Mode (Sample Environment)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+068
Tensile load frame
(force, torque)
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
Detectors, Monitors (neutron events)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085

## Slide 33: Flexible Chopper Veto
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+498
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
Chopper (TDC signal)
Detectors, Monitors (neutron events)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085
+495
+510
+510
+500
Nominal Value
+500
+500
+500
Notes: TDC signal could be an extra sensor outside the control electronics of the chopper motor:
Group results afterwards:
First class data -- 498
Second class data -- 495
Third class data -- 510
rubbish

## Slide 34: Diagnostics (Chopper Systems and Beam Transport)
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+498
Chopper 2 (TDC signal)
+497
+498
+495
+331
Chopper 1 (TDC signal)
+333
+330
+332
+xxx
+xxx
+xxx
+275
Monitor 1 (neutron events)
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+085
+xxx
+xxx
+xxx
+402
Monitor 2 (neutron events)
+xxx
+xxx
+xxx
+450
+xxx
+xxx
+xxx
+395
+xxx
+xxx
+xxx
+455
Chopper n (TDC signal)
Notes: One neutron monitor behind each chopper: neutron flux through window
Even think on a gamma monitor on the chopper, showing the effect of neutrons hitting the disc
Give time structure to monitor data and relate them to the corresponding
Use only monitor data within the time window (reduce background)
If considerable data is outside time window: Problem!
If number of counts is outside the ratio of

## Slide 35: Diagnostics (Wavelength Frame Multiplication Chopper)
Notes: In this case the count rate in all 5 monitors should be the same (minus the loss in the beam transport)
Or the sensitivity of the monitor has changed!

## Slide 36: Opportunities
Well defined modularity
Flexibility (Operation & Add-ons)
Higher availability
Better use of available beam time
Recover data
Advanced diagnostics

## Slide 37: Challenges & Risks
Handling large data streams
Failing of central services (like timing system)
New kind of data mining / data sorting SW necessary, has to be adapted to each functionality individually
Latency must be very well understood
Notes: I understand that we load a lot of responsibility to the SW people, in our case the DMSC
I know that in times of troubles there is always an arguing: is the problem on my side or on your side of the interface
But if we stand together from the beginning, develop and implement ideas together than I’m convinced we will succeed in presenting ESS users new capabilities in instrument control
If we have –straight from the beginning- the right HW in place, we can gradually implement the functionality of the instruments by implementing basic SW first and complement them with advanced features at a later stage.
And I would be very happy if we get input from you as experienced users for other new exiting use cases

## Slide 38: Time Stamping (Event Mode)
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
Detectors, Monitors (neutron events)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085

## Slide 39: Time Stamping (Event Mode)
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+498
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
Chopper (TDC signal)
Detectors, Monitors (neutron events)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085
+497
+498
+495

## Slide 40: Time Stamping (Event Mode)
AAZ1+000
AAZ2+000
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+498
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+068
Chopper (TDC signal)
Detectors, Monitors (neutron events)
Strain Scanner (force, torque)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085
+497
+498
+495

## Slide 41: Time Stamping (Event Mode)
+151
AAZ1+000
AAZ2+000
+651
AAZ3+000
AAZ4+000
ESS Timing System, 14 Hz
(Proton Pulse)
+498
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+079
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+068
Chopper (TDC signal)
Detectors, Monitors (neutron events)
Strain Scanner (force, torque)
Motion Control (positions)
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+098
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+036
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+xxx
+085
+497
+498
+495
+151
+651
+151
+651
+151
+651