## Slide 1: EPICS V4 for SNS Neutron Data
Kay Kasemir
Oct. 2014

## Slide 2: Basic Idea: V4 for Raw Neutron Data
Neutron Detector
Data Collection
Nexus File
Neutron Stats
Neutron Count, XY Histogram, Time-of-Fight Histogram
{ pixel, time-of-flight }
User Display
CS-Studio
Experiment Control
IOCs, pcaspy, ScanServer
Channel Access
n
n

## Slide 3: “V4”
pvData – Structured Data
  Java, C++
  Normative Types: Structs w/ time, alarm, ..
pvAccess – Network protocol
  Similar to CA
    Search via UDP 5076
    Connect by default on TCP 5075
  Server decides on byte order
  Partial transfers, whatever client requests
  Clever ‘size’: 1 byte if <255, …
Active development, protocol freeze in Oct. 2014

## Slide 4
Orig. SNS neutron network protocol | V4 pvData, pvAccess
‘events’ via UDP broadcast to any number of listeners | ‘monitors’ via TCP to 2-3 listeners
Protocol documented in code | Protocol documented in specification
Custom MS Visual C++ code took years to get stable | Java, portable C++, python code with wider developer and user base
No ‘debug’ tools | pvinfo, pvget, CSS Probe, …
Clients receive neutron events | Clients can see last (=stale) value, then new events
Can put anything into network package | Need to fit into pvData

## Slide 5: SNS Neutron Data
uint64 eventID uint64 pulseID // timeStamp double protonCharge struct
{ uint32 time_of_flight uint32 pixel } events[]

## Slide 6: SNS Neutron Data as pvData
Structure // Time stamp for all; // eventID in .userTag time_t timeStamp NTScalar protonCharge double value NTScalarArray time_of_flight uint[] value NTScalarArray pixel uint[] value NTScalarArray position_x uint[] value .. a few more optional elements

## Slide 7: What you get for free

## Slide 8: Tests
Server that generates fake neutron events
  Similar to pvDatabaseCPP example
  Can run standalone or in V3 IOC
“pvget –m” for initial tests
  Hit CPU limit because of string formatting
Custom client
  Tests for missing ‘event ID’
Results:
  Saturating 1GB network around 15M SNS events/sec
    100 updates/sec, each with 150000 events
    1 ‘event’  T.o.F + pixel  8 bytes, and indeed about 8 b/evt on network!!
  On 10GB network 100M SNS events/sec w/o problems
    Limit was CPU load, not network
  Required for SNS: 10M events/sec?

## Slide 9: Plan
Neutron Detector EPICS IOC, “nED” driver w/ pvAccess srv
Data Collection pvAccess client
Area Detector
“ADnED” pvAccess client, XY Pixel Histogram, Time-of-flight histogram, std. ROI, Array, … plugins
pvAccess
n
n
User Display
CS-Studio
Experiment Control
IOCs, pcaspy, ScanServer

## Slide 10: Looking Good!
  Can package data in flexible ways
  Already have network tools to inspect, monitor
  Performance is good
  Community of developers and users
    Thanks to Matej Sekoranja, Marty Kraimer, David Hickin for fast bug fixes and help