## Slide 1: The use of EtherCAT with EPICS at Diamond
Ronaldo Mercado
22/10/2014

## Slide 2
Contents
EtherCAT
Diamond setup
  Hardware
  EPICS driver
Recent work and work in-progress
  Screenshots from actual setup

## Slide 3
Why EtherCAT?
How does it work?
  EtherCAT master startup of LRW cycle
EtherCAT

## Slide 4
Open protocol, uses standard Ethernet hardware
Uses standard Ethernet cable and connectors. Can use standard switches and routers. DLS uses separate cabling - fieldbus.
Available Linux open source master.
Faster than most other fieldbuses.
Why EtherCAT?

## Slide 5
IEC 61138 (Type 12)
EtherCAT frame structure

## Slide 6
EtherCAT: Principle of operation
Master – slave communications with a periodic scan cycle
All operations in hardware, using an FPGA or an ASIC
Global addressing
Messages processed on the fly. One pass on the way out and on return – used for distributed clocks timing..

## Slide 7
Picture by EtherCAT Technology Group

## Slide 8
Configure FMMU for LRW packets
Master startup

## Slide 9
Contents
EtherCAT
Diamond setup
  Hardware
  EPICS driver
Recent work and work in-progress
  Screenshots from actual setup

## Slide 10
Channel
Access
Clients
Experimental Remote I/O
TCP/IP
Various networks
1U PC IOC
PCIe EVR
Timing interface panel
Timing system
IOC Remote I/O Network
PLC Equipment
Video
Motion
Remote IO
Modules
Other

## Slide 11
Hardware: Master and slaves

## Slide 12
IOC
Remote I/O
Fieldbus
(EtherCAT)
Remote IO
Modules
Beamline network
(TCP/IP)
View at the back of a server

## Slide 13
View at the back of a Front End server
IOC
Remote I/O
Fieldbus
(EtherCAT)
Remote IO
Modules
Instrumentation Network
(TCP/IP)
Controls Network
(TCP/IP)

## Slide 14
Contents
EtherCAT
Diamond setup
  Hardware
  EPICS driver
Recent work and work in-progress
  Screenshots from actual setup

## Slide 15
EtherLab Master
  www.etherlab.org
  Open source, GPLv2
  Realtime Linux (RTAI, Preempt_RT and others)
  Part of Etherlab, marketed by IgH (Germany)
EtherCAT Scanner (Master)

## Slide 16
Kernel module
User space and kernel space API
Generic and hardware specific network driver
FMMU setup and slave state machine control
Scan timer not provided. Using 1 KHz. 10 KHz possible.
Configuration not provided
Etherlab Master

## Slide 17
Standard Ethernet Driver
Network Stack
Generic Ethernet Driver Module
EtherCAT Master Module
libethercat
Hardware (Network Interface Card)
Fieldbus Scanner
EPICS IOC
EPICS Records
Asyn Driver
Kernelspace Preempt RT Linux Kernel
Userspace
Hardware
Etherlab (Master)
EPICS IOC
EPICS Records
Asyn Driver
EPICS IOC
EPICS Records
Asyn Driver
Diamond ethercat
Diamond EtherCAT Driver

## Slide 18
EtherCAT integrated into EPICS. Uses
  PREEMPT_RT Linux
  Etherlab Ethercat Master for Linux
  Asyn
Scanner broadcast bus data to several Soft IOCs for segregation of areas. Automatic Asyn port creation
  One port per slave
  One port for master status
Diamond EtherCAT Driver

## Slide 19
Recent work and work in progress
PDO assignments
SDO read/write
Worst Case Response Time patch
Interfacing to Beckhoff Embedded PC CX9020

## Slide 20
PDO assignment in screenshots

## Slide 21
SDO configuration

## Slide 22
Worst Case Response Time
Reduce WCRT from 3 to 2 (Damien Lynch, ANSTO)

## Slide 23
Interfacing to CX9020
Work by Damien Lynch at ANSTO
Adds Float64 data type

## Slide 24
Thank you for listening!
http://controls.diamond.ac.uk/downloads/support/ethercat/
Thanks to:
James Rowland
Linda Pratt
Peter Leicester
Tom Cobb
Ian Gillingham
Andy Foster
Damien Lynch (Ansto)
Kevin Wilkinson
Armin Wagner