## Slide 1: Integrating high speed detectors at Diamond
Nick Rees,, Mark Basham, Frederik Ferner, Ulrik Pedersen, Tom Cobb, Tobias Richter, Jonathan Thompson… (Diamond Light Source),
Elena Pourmal (The HDF Group)

## Slide 2: Introduction
History
Detector developments
  Parallel detectors
  Spectroscopic detectors
HDF5 developments
  HDF5 1.8.11 (Available now):
    Dynamically loaded filter libraries
    Direct write of compressed chunks
  HDF5 1.10 (Being integrated):
    New dataset indexing: Extensible array indexing.
    SWMR
    VDS
    Journaling

## Slide 3: History
Early 2007:
  Diamond first user.
  No detector faster than ~10 MB/sec.
Early 2009:
  first Lustre system (DDN S2A9900)
  first Pilatus 6M system @ 60 MB/s.
Early 2011:
  second Lustre system (DDN SFA10K)
  first 25Hz Pilatus 6M system @150 MB/s.
Early 2013:
  first GPFS system (DDN SFA12K)
  First 100 Hz Pilatus 6M system @ 600 MB/sec
  ~10 beamlines with 10 GbE detectors (mainly Pilatus and PCO Edge).
Late 2015:
  delivery of Percival detector (6000 MB/sec).
Chart: 
| 2007 | 2009 | 2011 | 2013 | 2015
Peak Detector Performance (MB/s) | 10 | 60 | 150 | 800 | 6000
Doubling time = 7.5 months
Notes: I02, I03, I04, I24, I22, B22, I12, I13

## Slide 4: Detector developments

## Slide 5: Diamond Detector Model

## Slide 6: Potential EPICS Version 4 Model

## Slide 7: Basic Parallel Detector Design
Readout nodes all write in parallel
Need a mechanism to splice data into one file.
FEM
FEM
FEM
FEM
FEM
FEM
Detector head
Sensor/Medipix3 Hybrids
Readout Node
Readout Node
Readout Node
Readout Node
Readout Node
Readout Node
Control Process
10GigE
Optical Links
Network

## Slide 8: Detector Block Diagram
Detector Wire Protocols
Data Receiver
Data Processing:
2 bit gain handling
DCS subtraction
Pixel re-arrangement
Rate correction(?)
Flat field
Dark subtraction
Efficiency correction
Data Compression
HDF5 File Writer
Detector API
Detector Control
Configuration
Control Driver
Cmd
HDF5 file
HDF5 file
Calibration
Software
Tango/ Lima
EPICS/ Area Detector
Detector Control Software
Detector Data Stream (n copies)
Documented
Controlled
Interfaces
Beamline Control Software
Detector Engineer Software
Actual/potential network or CPU socket boundaries
Detector Array
Control Server
Status

## Slide 9: Spectroscopic Detectors
areaDetector is poorly named…
  Base class is asynNDArrayDriver, but this name is not so catchy…
    NDArray* classes provide basic functionality
    Core plugins derive from NDPluginDriver and many will work with any NDArray.
    Most popular plugins are the file writing plugins that get data to disk.
  Basic areaDetector class is really NDDriver
    Provides methods for reading out a typical areaDetector
    The methods aren’t so good for other types of detectors, e.g.:
      Spectroscopic (MCA like) detectors.
      Analogue (A/D like) detectors.

## Slide 10: Proposal for new ND Drivers
Need a set of basic driver classes for other types of NDArrays
  NDMCADriver (or NDSpectraDriver)
    Generates 2-D array of energy vs detector channel
    3rd dimension can be time.
  NDADCDriver (or ND DigitizerDriver)
    Generates 1D array of values from a set of ADC’s
    2nd dimension can be time.
Each driver can feed existing plugins, but also could benefit from specialist plugins.

## Slide 11: Updated NDFileHDF5 plugin
Provides control of HDF5 chunking and compression features.
Now can define the HDF5 layout with an XML file.
  Data source can be detector data, NDAttributes or constant.
Can write any HDF file format – e.g. NeXus or Data Exchange.
Collaboration between Diamond and APS

## Slide 12: HDF5 Developments

## Slide 13: HDF5 key points
HDF5 is mature software that grew up in the HPC environment.
It is a widely used standard and has the richest set of high performance functionality of any file format.
It allows rich metadata and flexible data formats
It has some caveats we know about:
  HDF5 is single threaded.
  pHDF5 relies on MPI, which doesn’t happily co-exist with highly threaded architectures like EPICS.
  pHDF5 is not as efficient as HDF5
  pHDF5 doesn’t allow compression.
  Files cannot be read while they are written

## Slide 14: Recent Developments: Release 1.8.11
H5DO_write_chunk
  Funded by Dectris and PSI
  Improves writing compressed data by:
    Avoiding double copy of filter pipeline
    Allowing optimised (e.g. multithreaded) compression implementations
Pluggable filters
  Funded by DESY
  Allows users to provide filters as a shared library that is loaded at runtime.
  Search path set by environment variable: HDF5_PLUGIN_PATH

## Slide 15: Chunk write mechanism

## Slide 16: Current developments: Release 1.10
File format changes that need a major release:
  Improved dataset indexing:
    New B-Tree implementation
    Extensible array indexing
  Journaling
  Virtual Object Layer
  Single Writer Multiple Reader (SWMR)
    Funded by Diamond, Dectris and ESRF
  Virtual Data Set
    Funded by Diamond, DESY and Percival Detector
Beta release July 2015

## Slide 32: Thank you for your attention…