## Slide 1: Tools and Services at NSLSII
Kunal Shroff, Tasha Summers, Smith Reid, Gabriele Carcassi, Michael Davidsaver (NSLSII)
Ralph Lange (ITER)
Samuel Dallstream (UMich)
Michael Skinner (Marist College)

## Slide 2
Publish/subscribe
CSS
IOC
CA client (JCA/CAJ)
IOC
…
IOC
pvA client
IOC
…
v3
v4
…
AccelUtils
Command/response
v4
Masar
Web based REST services
...
Olog
ChannelFinder
API
API
…
API
…
pvmanager core
pva
…
ca
Data Sources
Processing
Visualization
vTypes
Data Definition
BOY
cf
Aggregation
General purpose clients
Specialized clients
Log Viewer
Channel Viewer
DataBrowser
…
…
formula
graphene
…
Registry
Bindings
pvm services
masar
CSS core
WebUI, scripts, other client
...
cf-update
Logbook
Core Java Client
NEW!
NEW!

## Slide 3
Publish/subscribe
IOC
CA client (JCA/CAJ)
IOC
…
IOC
pvA client
IOC
…
v3
v4
…
AccelUtils
Command/response
v4
Masar
Web based REST services
...
Olog
ChannelFinder
API
API
…
API
…
pvmanager core
pva
…
ca
Data Sources
Processing
Visualization
vTypes
Data Definition
cf
Aggregation
formula
graphene
…
Registry
Bindings
pvm services
masar
WebUI, scripts, other client
...
cf-update
Logbook
Core Java Client
NEW!
NEW!
CSS
BOY
General purpose clients
Specialized clients
Log Viewer
Channel Viewer
DataBrowser
…
…
CSS core

## Slide 4: CS-Studio
An Integrated platform for controls and physics applications
  Over 2 dozen releases
  In production 3.1.6, 3.2.15a, and 3.3.10a

## Slide 5: CS-Studio Applications
BOY
BEAST
LogViewer
DataBrowser
Pretune
ShiftViewer

## Slide 6: BOY: Best OPI Yet
Approximately 5000 opi screens
All hosted in a mercurial repository
NFS mounted onto all machines in the controls network

## Slide 7: BOY Screens
Engineering :
  Developed by the controls engineers / the developers of the device IOC
  Designed for device control
Physics:
  Do the real useful stuff..
  Created from a list of required interfaces and discussed in AP group meetings
  Lots of rules, calls to external python scripts
  Task oriented screens
Operator:
  Combine/Summarize a lot of information

## Slide 8: Issues Interesting Experiences

## Slide 9: BOY Screen standards:
A perfect standards are hard to define
Following standards adds overhead
Source: http://xkcd.com/927/

## Slide 10: Absence of BOY Screen standards:

## Slide 11: Solution*
Guidelines are easier than standards
Good examples more effective then good standards
* contingent on cooperation between physicist, engineers and operators

## Slide 12: Good and Bad Practices:
PV naming convention + Macros + Linking containers
  Reusable pieces
  Easily modified

## Slide 13: Good and Bad Practices:
PV naming convention + Macros + Linking containers + Rules
  2000 + pvs with over 800 rules
Solution:
  Multistate LED + formulas

## Slide 14: Good and Bad Practices:
Avoid Scripts/Rules unless absolutely necessary
  Should this be implemented in an IOC?
  Is there a PvManager formula I can use?
  Can I use rules? (Have I allocated a large enough PermGen space)
  Use a script

## Slide 15: Data Connection Layer:
3.1.x
  Use PVManager to address threading issues, source rate throttling
3.2.x
  PVManager with formula functions to provide and alternative to rules and scripts
  Graphene prototype for displaying large waveforms
3.3.x
  Passive scanning: switch from active polling of the queue to notification model
  More graphene plots

## Slide 16: SWT:
A limited widget set
  Using native widget results in the lowest common denominator
  Poor performance on Linux machines
JavaFX to the rescue
  Part of jdk 8
  Richer and easier to use widget set
    TreeTable, Table with embedded controls
  JavaFX and SWT share the UI thread
    Can be easily embedded into SWT/Jface composites/views

## Slide 17: JavaFX in eclipse
Share the same UI thread
Relatively easy to embed
  Require e(fx)clipse
Notes: Unfortunately, JavaFX was not written with OSGi in mind so there are various sources of error when running inside OSGi. These problems include the location of the JavaFX binaries in your Java installation and class loading issues because of OSGi's visibility rules. e(fx)clipse provides helper libraries for dealing with all of those problems and makes writing JavaFX applications on top of Eclipse Equinox feel as easy as it is with SWT and Swing.

## Slide 18: JavaFX preliminary comparisons
1000 label widgets updating at 1Hz
Notes: The goal of this experiment was to measure the difference in performance between JavaFX and SWT when drawing many objects on a screen. In order to test performance, a program was written in both JavaFX and SWT that draws multiple text objects in an eclipse view and updates them using a PV. Windows Performance Monitor was used to monitor the CPU Load, and all tests were completed within the Windows 8 operating system.

## Slide 19
Publish/subscribe
IOC
CA client (JCA/CAJ)
IOC
…
IOC
pvA client
IOC
…
v3
v4
…
Command/response
v4
Masar
...
…
API
…
pvmanager core
pva
…
ca
Data Sources
Processing
Visualization
vTypes
Data Definition
Aggregation
formula
graphene
…
Registry
Bindings
pvm services
masar
Core Java Client
NEW!
NEW!
CSS
BOY
General purpose clients
Specialized clients
DataBrowser
…
…
CSS core
Olog
API
...
Logbook
Log Viewer
ChannelFinder
API
cf
WebUI, scripts, other client
cf-update
Channel Viewer
AccelUtils
Web based REST services

## Slide 20: Motivation and Objectives
A flat name space restricts seriously:
  Clients need to know all channel names beforehand
  Portable generic clients must be simple
  Apps need full configuration or framework supplied service
Develop a Directory Service
  Generic
    No dependency on installation and local conventions
  Simple and fast (enough)
    Use standards wherever possible
  Provides "query-by-functionality"

## Slide 21: Directory Data
Set of Channels (unique names)
Each Channel has an arbitrary number of Properties (name/value pairs) and Tags (names)
Each Channel, Property, or Tag has an Owner (group) to allow basic access control
All names and values are strings

## Slide 22: Directory Data example
<channel name="V:1-SR-BI:SUPER{BPM:4}SA:X" owner="cf-update">
<properties>
<property name="elemName" value="bpm:4" owner="cf-update"/>
<property name="elemIndex" value="400" owner="cf-update"/>
<property name="elemPosition" value="5.208" owner="cf-update"/>
<property name="pvStatus" value="Active" owner="cf-update"/>
</properties>
<tags>
<tag name="aphla.sys.SR" owner="operator"/>
</tags>

## Slide 23: Query Example
SR:*C01*
  All pvs from storage ring cell 1
SR:*C01*&elemName=bpm:4*
  All pvs from storage ring cell 1 belonging to element bmp:4
SR:*C01*&elemName=bpm:4*&pvStatus=active
  All pvs from storage ring cell 1 belonging to element bmp:4 and with pvStatus active
SR:*C01*&elemName=bpm:4&tag=aphla.sys.SR
  All pvs from storage ring cell 1 belonging to element bmp:4 with tag aphla.sys.SR

## Slide 24
Publish/subscribe
IOC
CA client (JCA/CAJ)
IOC
…
IOC
pvA client
IOC
…
v3
v4
…
Command/response
v4
Masar
...
…
API
…
pvmanager core
pva
…
ca
Data Sources
Processing
Visualization
vTypes
Data Definition
Aggregation
formula
graphene
…
Registry
Bindings
pvm services
masar
Core Java Client
NEW!
NEW!
CSS
BOY
General purpose clients
Specialized clients
DataBrowser
…
…
CSS core
Olog
API
...
Logbook
Log Viewer
ChannelFinder
API
cf
Channel Viewer
AccelUtils
Web based REST services
Python hla scripts
WebUI, scripts, other client
cf-update

## Slide 25: Populating ChannelFinder
cf-update
  Adds new channels
  Manages existing channels
    Orphaned channels
    Moved channels
Python scripts
cf-properties (under development)

## Slide 26: Example st.cmd
dbLoadRecords("gauss.db","P=ktest")
epicsEnvSet("EPICS_HOSTNAME", "dev32new")
epicsEnvSet("EPICS_IOCNAME", "gauss")
iocInit()
# pipe the output of the dbl command to a file
# the file name should follow the convention 'myHostName.myIOCName.dbl'
# write the file to a well know directory on which the cfmonitor deamon is running
dbl > $(CF_UPDATE_DIR)/$(EPICS_HOSTNAME).$(EPICS_IOCNAME).dbl

## Slide 27: Under the Hood
The cf_monitor daemon monitors $(CF_UPDATE_DIR) directory and envokes an updare task when
  A new *.dbl file is created in the dir
  An existing *.dbl file is modified
The update task handles
  Uses the filename to obtain the hostName, iocName property values
  New channels – creates new channels with hostName, iocName, pvStatus and time properties
  Orphaned channels – pvStatus property is updated
  Moved channels – ensures that the hostName, iocName properties are update when channels are moved
  Unchanged channels
In all cases existing properties(excluding hostName, iocName, pvStatus, time) and tags are left unaffecteds

## Slide 28: device FM1G4C02A
Channel Name | SR:C02-MG:G04A{HFCor:FM1} Fld-I | SR:C02-MG:G04A{HFCor:FM1} Fld-SP | SR:C02-MG:G04A{HFCor:FM1} Fld-I | SR:C02-MG:G04A{HFCor:FM1} Fld-SP
handle | READBACK | SETPOINT | READBACK | SETPOINT
elemName | FXM1G4C02A |  | FYM1G4C02A | 
elemType | HFCOR |  | VFCOR | 
elemField | x |  | y | 
devName | FM1G4C02A |  |  | 
sEnd | 65.5222 |  |  | 
cell | C02 |  |  | 
girder | G4 |  |  | 
symmetry | A |  |  | 
length | 0.044 |  |  | 
ordinal | 263 |  | 264 | 
tags | eget | eput | eget | eput
 | x |  | y | 
 | sys.SR |  |  | 
Notes: From Linyun Yang (accelerator physics) talk:
  From Channel Access to Channel Finder Service:
    Channel Accesses in Python and Matlab are simple to use.
    High level applications (HLA) deals with thousands of magnets, instruments and more channels.
    Organized/structured channel information is necessary.
    Channels linked to accelerator lattice and diagnostics are even better.
    Searching instead of remembering is easier for HLA users.
A “dictionary” service can help HLA to manage the channels and build a lattice structure to which the AP is familiar. (they done simulation, analysis with it in the design).
Physics group can re-create the lattice from the information in channel finder
By tags, different lattices can be built, and elements can be shared between them.
  Sharing is important for injection, where LTD1 and LTD2 shares a lot of elements with LTB

## Slide 29: ChannelViewer

## Slide 30: Auto-complete

## Slide 31: PVManager Formula
=cf(“* elemType=HFCOR handle=SETPOINT tags=sys.SR”)
Queries ChannelFinder and returns a VTable consisting of all of channels for the setpoint pvs for all horizontal fast correctors in the storage ring

## Slide 32: Even more Interesting Experiences

## Slide 33: ChannelFinder data
Over 180k channels
Over 1.2 million instances of channel + tag/property
Service response (Query + Parsing) in the order of seconds

## Slide 34: MongoDB
Embedded (denormalized) data model
  Ideal for one-to-many relationships between entities.
  provides better performance for read operations, as well as the ability to request and retrieve related data in a single database operation.
  Embedded data models make it possible to update related data in a single atomic write operation.
// channels
{
  name: “channel name”
  owner: “channel owner”
  properties: [{name: “property name”,
  owner: “property owner”,
  value: “property value”,
  _id: properties._id},......]
  tags: [tags._id,.....]
}
// tags
{
  name: “Tag name”,
  owner: “Tag owner”,
  _id: ID
}
// properties
{
  name: “Property name”,
  owner: “Property owner”,
  _id: ID
}

## Slide 35: Performance Environment
Database
  150k channels
  15 million channel-properties/channel-tags
Queries
  Search based on channel names and property values

## Slide 36: Mysql Vs MongoDB
Mysql
MongoDB

## Slide 37: Questions?

## Slide 38: Links:
Control System Studio
  http://controlsystemstudio.org/
ChannelFinder
  http://channelfinder.sourceforge.net/
  https://github.com/ChannelFinder/ChannelFinderService
Performance Tests
  https://github.com/shroffk/cf-mongo-java-test
  https://github.com/mskinner5278/cf-mongo-test
JavaFx
  https://github.com/sjdallst/FXvsSWTProfiling
  http://www.eclipse.org/efxclipse